## Slide 1: Final Presentation
Jacob Heglund
AE 598 – Advanced Navigation Systems

## Slide 2: Motivation
Original Project Goal – Way too ambitious
  Develop a simulated autonomous car that could solve the navigation task in an environment filled with obstacles
Modified Project Goal – Too many different topics
  Examine low-level and high-level navigation tasks

## Slide 3: Motivation
Final Project Goal
  Develop end-to-end pipelines for detecting lane lines from camera images on a road vehicle
  Learn about classical CV and it’s application in modern autonomous vehicles

## Slide 4: Work Done
Developed three pipelines for detection of lane lines
  Each builds on the techniques developed in the last iteration
  Each pipeline utilizes classical CV methods, no deep learning
All data taken from a front-mounted camera on a car on the highway
  This simplifies the problem, only dealing with 1 sensor

## Slide 5
Results

## Slide 6
Pipeline #1

## Slide 7: Pipeline #1 – Outline
Identify lanes based on 2 factors
  position
  color

## Slide 8: Pipeline #1
Region of Interest
  Assumptions
    The lane lines up with the front of your car
  Assumption Breaks
    Going up a steep hill
    Sharp corners
    No visible lane lines
    Your car is upside down

## Slide 9: Pipeline #1
Color Threshold
  White and yellow are bright in the R channel of RGB color space
    Set a threshold that only leaves the lane marker pixels
  Can also examine other color spaces (HSV, LUV, LAB)

## Slide 10: Pipeline #1

## Slide 11: Pipeline #1 - Discussion
Even with a simple pipeline, there are several parameters we could tune
  Region of interest size can be adaptive
  How to select a color threshold?
    What if it is a cloudy day?
    What if night time? Street lights?
This method doesn’t clearly define a lane
  We have only identified pixels that may or may not be at the edge of the lane

## Slide 12
Pipeline #2

## Slide 13: Pipeline #2 – Outline
Want to identify groups of pixels that fit along edges
  Region of Interest
  Grayscale + Gaussian Blur
    Improves edge detector performance
  Canny Edge Detection
  Hough Transform
    This finds lines at a certain angle within the image

## Slide 14: Pipeline #2
Starting Image

## Slide 15: Pipeline #2
Region of Interest + Grayscale + Gaussian Blur

## Slide 16: Pipeline #2
Canny Edge Detection
  Finds areas of high gradient in the image
  Very similar to a Sobel edge detector

## Slide 17: Pipeline #2
Canny Edge Detection

## Slide 18: Pipeline #2
Hough Transformation – OpenCV
  searches image for lines with a particular slope and intercept
  allows you to choose the minimum line length and max gap
  returns a set of lines
    if positive slope, the line is part of the left lane marker
    if negative slope, the line is part of the right lane marker
Assumptions
  The lane markers are all running roughly in the same direction
  The lane markers have consistent spacing
Assumption Breaks
  Construction zones
  Corners

## Slide 19: Pipeline #2
Take the average of all points in the lane marker, and find the best linear fit through these points
  this linear fit will be our best approximation of the lane marker
Color the region between these two lines

## Slide 20: Pipeline #2

## Slide 21: Pipeline #2 – Discussion
This method clearly improves by defining the lane boundaries
  The method of line fitting is still very rudimentary
Applies more generalizable techniques
  Fewer tunable parameters
Works well for still images, fast vehicle motion is filtered by averaging
  The lane detector can be slow to respond
  Application of Kalman filter w/ motion model of the vehicle?

## Slide 22
Pipeline #3

## Slide 23: Pipeline #3 – Outline
Use a more sophisticated method for identifying pixels in the lane lines
  Binary Pipeline
    Undistort (lens curvature)
    Perspective Transform
    Color Spaces
    Canny Edge Detection
  Line Fitting Pipeline
    histogram
    sliding windows for pixel detection

## Slide 24: Pipeline #3
Correct for curvature in the camera lens
  This will make the perspective transform easier to interpret

## Slide 25: Pipeline #3
Perspective Transform
  Turn the “lane points” into a rectangle
    Car perspective -> birds-eye perspective
  Allows easier enumeration of pixels in the lane line
  Fewer pixels per area further from the camera, leads to distortion

## Slide 26: Pipeline #3
Perspective Transform

## Slide 27: Pipeline #3
Color Spaces + Canny Edge Detection
  Gives a binary image
Take a histogram of white pixels along the x-axis

## Slide 28: Pipeline #3
Sliding Windows Method
  Identifies lane pixels that are not necessarily in a straight line
    Start with the histogram peaks as window center
    Move up N pixels, recompute the mean x-position

## Slide 29: Pipeline #3

## Slide 30: Pipeline #3
Fit 2nd order polynomial through lane pixels in a frame, and reverse the perspective transformation

## Slide 31: Pipeline #3
Job done? Not quite
  Changing light conditions pose a challenge for our detector

## Slide 32: Pipeline #3
Developed a pipeline that works well for highway situations
  Light conditions don’t change rapidly
  There are no quick turns
Pedestrians and other vehicles are not yet considered

## Slide 33: Conclusions
Many heuristics in computer vision
  Each problem has different valid assumptions
  Human intuition is still an important part of the field
  CV algorithms tend to have many tunable parameters
CNNs performs well in object recognition tasks
  However, a well-designed CV pipeline can be just as effective, especially in prototyping stages
  CV can also be easier to debug and requires fewer overall resources (datasets, computation, etc.)

## Slide 34: Remaining Work
Improve robustness of classical CV in challenging situations
  Particularly when shadows cover the road
  Tuning parameters for different situations
Implement a detector performance metric and compare the accuracy of my implementations

## Slide 35: Questions?